## Slide 1: Physical modelling of embedded systems EL044A
Advanced Spice modelling
Electric/Electromagnetic and coupled physical effects

## Slide 2: Physical analysis
Simulations
  Mechanical
  Electrical
  EMC
  Thermal
  System dynamics
Set of tools
Finite element method (FEM)
  COMSOL Multiphysics
  ANSYS
  CATIA
Circuit models
  SPICE
Behavioural analysis tools
  Imagix 4D
  Sniff+
Notes: Mec: Vibration, mechanical shocks, material properties, failures
Elec: circuit modelling
EMC: fields, generation, interfecrence
Thermal: joule heating and so on
System dynamics

## Slide 3: Physical analysis
Simulations
  Mechanical
  Electrical
  EMC
  Thermal
  System dynamics
Set of tools
Finite element method (FEM)
  COMSOL Multiphysics
  ANSYS
  CATIA
Circuit models
  SPICE
Behavioural analysis tools
  Imagix 4D
  Sniff+
Notes: Mec: Vibration, mechanical shocks, material properties, failures
Elec: circuit modelling
EMC: fields, generation, interfecrence
Thermal: joule heating and so on
System dynamics

## Slide 4: LTspice
Powerful spice simulator software from Analog Devices
  Developed by Linear Technologies acquired by Analog Devices
  Developed for efficient transient simulations but handles AC and DC sweeps and Noise analysis as well
  http://ltwiki.org/
  http://www.analog.com/en/design-center/design-tools-and-calculators/ltspice-simulator.html

## Slide 5: Electro / Electromagnetic coupling and EMI
Electric coupling
  Potential changes in a circuit couples through parasitic capacitances
  Sensitive for large dV/dt
  Capacitance
  Modelled in Spice as a behavioral current source
Magnetic Coupling
  Current in wires induced magnetic fields that couples to other nearby wires.
  Sensitive to large dI/dt
  Inductance
  Behavioral Voltage source in spice

## Slide 6: Coupled physical effects
In some cases external physical effects may affect the circuit itself and needs to be modelled for study and/or design of a system.
Examples
  Losses in a device/system increase the junction temperature of semiconductor.
  The resistance of a heating element changes when the temperature raises
  A sensor that convert one physical unit to voltage or current
  Simulation of Motors and Generators and its drives
  Kinetic energy is converted into electrical energy in regeneration breaking

## Slide 7: Thermal modelling
Thermal resistance
L – Length
A – Cross sectional area
k- Material thermal conductivity
Thermal spreading approx 45°
R=ρL/S
Notes: Draw simple transistor, 2x2mm 0.3mm thick… Cu - Base plate 1mm 1x1 cm (limited by spreading) - Isolator 1x1 cm (spreading) – Heat sink

## Slide 8: Dynamic thermal modelling
Thermal capacitance
m=thermal mass
Notes: Draw and discuss a lumped part with thermal spreading

## Slide 9: Coupled electro-thermal transistor modelling
Simulate first with only thermal resistance
Add thermal capacitances and surge
https://gansystems.com/wp-content/uploads/2018/02/GS66516B-DS-Rev-180213.pdf
Simulate first with only thermal resistance
Add thermal capacitances and surge(浪涌)
https://gansystems.com/wp-content/uploads/2018/02/GS66516B-DS-Rev-180213.pdf

## Slide 10: High temperature resistive heating
At high T R=f(T) should be considered in an accurate model.
  Variable resistance i required
  Current source dependent of the voltage across it.

## Slide 11: System Analogies